Yuba County Water Agency - FERC Relicensing

Feather River Ranger District, Plumas National Forest

Cottage Creek Small Group Campground

Schematic Design Review 2

Reviewers:  Jared Pierce (TNF Landscape Architect), TNF/PNF District Rangers and Recreation Staff

Date:  12/10/2015

Comments below are in response to a site visit conducted on 10/16/15 and an updated schematic design plan developed by MHM Inc., dated 10/30/2015.

- The width of the phase one loop does not need to be 37’ wide.  To prevent extra vehicle parking in the loop road, a road width of at least half that should be sufficient.  A wider road width may still be useful near site one to accommodate turning radii.

- Not enough space is given to the water point between sites 1 and 2.  To allow for more space for this water point, the single vehicle parking spaces may need to be moved to opposite side of the RV parking pad.

- Site 2 should also be ADA accessible (in a campground of this size, 2 campsites should be ADA accessible, see FSORAG).

- The host site septic tank should be located closer to the west side of the host site parking pad to allow for better concealment and a shorter hose run.