## Slide 1
Licensee Response to Relicensing Participant
Tunnel Closure Proposal
Agency/NGO Yuba River
Development Project (FERC Project No. 2246)
Relicensing Participant’s Proposal Response to YCWA Counter Proposal
08/11/15

## Slide 2: Summary of RPs’ 11/13/14 Proposal
Current RPs’ proposal regarding flows upstream of Englebright:
  Same WY types as those in Forest Service’s final FPA 4(e) Conditions for upstream hydro Projects
  Minimum flows at Our House, Log Cabin and NBB Dams
    NBB Minimum Flows are RPs’ 9/24/13 proposed minimum flows; not RPs’ 2/27/15 proposed NBB minimum flows that are contingent on reaching agreement on LWM placement and sediment injection in NBB Reach - agreement hasn’t been reached.
  Sediment transport pulse flows at Log Cabin and our House
  Whitewater boating pulse flows at Our House
  Close Lohman Ridge and Camptonville tunnels from April 1 through September 30 in any year when NBB storage is 780,000 ac-ft or more on March 31
  4-week long spill cessation at Our House and Log Cabin beginning on April 1 in years when tunnels not closed
See Model Run RP111314

## Slide 3: Tunnel Closure Years Under RPs’ 11/13/14 Proposal (both tunnels)
Water Year | Rank in POR Based on April Water Year Forecast (1970-2015) (wettest = 1) | Reduction in Water Diversion (TAF & % of WY total) | Reduction in NBB Spill Volume (TAF & % of WY total) | Reduction in Diversion Days (Days & % of WY total) | Reduction in Total Generation (GWh & % of WY total)
1983 | 1 | 179 (48%) | 80 (15%) | 153 (50%) | 114 (4%)
1982 | 2 | 141 (41%) | 112 (17%) | 103 (37%) | 40 (2%)
1995 | 3 | 165 (54%) | 89 (22%) | 114 (44%) | 86 (4%)
1974 | 5 | 128 (39%) | 12 (4%) | 112 (42%) | 139 (6%)
1986 | 6 | 76 (37%) | 0 (0%) | 82 (38%) | 90 (6%)
2006 | 7 | 128 (46%) | 114 (25%) | 89 (40%) | 16 (1%)
1998 | 10 | 134 (52%) | 70 (39%) | 116 (50%) | 75 (4%)
1993 | 13 | 90 (42%) | 7 (32%) | 102 (46%) | 98 (6%)
1971 | 15 | 108 (46%) | 0 (0%) | 111 (43%) | 131 (7%)
1996 | 18 | 111 (47%) | 30 (13%) | 100 (48%) | 97 (5%)
1989 | 20 | 59 (39%) | -20 (-57%) | 77 (35%) | 51 (4%)
Average of Above Years | -- | 120 TAF (45%) | 45 TAF (10%) | 105 Days (43%) | 85 GWh (4%)

## Slide 4: YCWA’s L062415 Counter-Proposal
YCWA’s counter-proposal includes three items on which it believes RPs and YCWA have tentative agreement:
  Same WY types as those in Forest Service’s final FPA 4(e) Conditions for upstream hydro Projects (agreement with RPs’ Current Proposal)
  Sediment transport pulse flows at Log Cabin and our House (modified as subsequently agreed to by RPs and YCWA, documented on Relicensing Website)
  Whitewater boating pulse flows at Our House (modified as subsequently agreed to by RPs and YCWA, documented on Relicensing Website)
YCWA’s counter-proposal includes:
  Minimum flows at Our House, Log Cabin and New Bullards Bar dams, as proposed by YCWA in its FLA
  Spill cessation at Our House in years when Lohman Ridge Tunnel not closed, and at Log Cabin and New Bullards Bar dams in all years, using spill cessation measure in YCWA’s FLA
  Close Lohman Ridge Tunnel (not Camptonville Tunnel) from April 11 through September 30 when both New Bullards Bar Reservoir storage is 780,000 ac-ft or more on March 31 and DWR’s April median water year forecast is greater than 3,600 TAF

## Slide 5: Tunnel Closure Years Under YCWA’s L062415 Counter-Proposal (only Lohman Ridge)
Water Year | Rank in POR Based on April Water Year Forecast (1970-2015) (wettest = 1) | Reduction in Water Diversion (TAF & % of WY total) | Reduction in NBB Spill Volume (TAF & % of WY total) | Reduction in Diversion Days (Days & % of WY total) | Reduction in Total Generation (GWh & % of WY total)
1983 | 1 | 132 (35%) | 64 (11%) | 127 (42%) | 78 (3%)
1982 | 2 | 109 (30%) | 78 (11%) | 103 (35%) | 33 (1%)
1995 | 3 | 104 (35%) | 73 (15%) | 113 (42%) | 37 (2%)
1974 | 5 | 111 (32%) | 8 (2%) | 108 (39%) | 119 (5%)
1986 | 6 | 68 (30%) | 0 (0%) | 84 (37%) | 78 (5%)
2006 | 7 | 89 (30%) | 70 (14%) | 96 (41%) | 21 (1%)
Average for Above Years | -- | 102 TAF (32%) | 49 TAF (9%) | 105 Days (39%) | 61 GWh (3%)

## Slide 6: Summary of RPs’ 08/11/15 Proposal
  Same WY types as those in Forest Service’s final FPA 4(e) Conditions for upstream hydro Projects
  Minimum flows at Our House, Log Cabin and NBB Dams
    NBB Minimum Flows are RPs’ 2/27/15 proposed NBB minimum flows
    (with the understanding that gravel and wood plans will be agreed upon)
  Sediment transport pulse flows at Log Cabin and our House
  Whitewater boating pulse flows at Our House
  Close Lohman Ridge tunnel from April 1 through September 30 in any year when NBB storage is 775,000 ac-ft or more on March 31, and DWR’s March median water year forecast is greater than 2,191 TAF
  Concurrent with Lohman Ridge Tunnel closure as described in #5, open low level outlet and fish release outlet valve at Log Cabin Diversion, but leave tunnel open
  4-week long spill cessation at Our House and Log Cabin beginning on April 1 in years when tunnels not closed, FLA NBB spill recession

## Slide 7: Summary of RPs’ 08/11/15 Proposal
  Same WY types as those in Forest Service’s final FPA 4(e) Conditions for upstream hydro Projects
  Minimum flows at Our House, Log Cabin and NBB Dams
    NBB Minimum Flows are RPs’ 2/27/15 proposed NBB minimum flows
    (with the understanding that gravel and wood plans will be agreed upon)
  Sediment transport pulse flows at Log Cabin and our House
  Whitewater boating pulse flows at Our House
  Close Lohman Ridge tunnel from April 1 through September 30 in any year when NBB storage is 775,000 ac-ft or more on March 31, and DWR’s March median water year forecast is greater than 2,191 TAF
  Concurrent with Lohman Ridge Tunnel closure as described in #5, open low level outlet and fish release outlet valve at Log Cabin Diversion, but leave tunnel open
  4-week long spill cessation at Our House and Log Cabin beginning on April 1 in years when tunnels not closed, FLA NBB spill recession

## Slide 8
 | WY TYPE | B120 March 1 forecast (TAF) | Original RP 111314 (both tunnels closed) | RP 111314 with model modifications (both tunnels closed) | L062415 (only Lohman Ridge closed) | RP081115 (only Lohman Ridge closed and LLO open at LCD) | 
Water Year | AN | 2590 | 1971 | 1971 |  | 1971 | 
 | AN | 3220 | 1974 | 1974 | 1974 | 1974 | 
 | AN | 2680 | 1978 |  |  | 1978 | 
 | W | 3770 | 1982 | 1982 | 1982 | 1982 | 
 | W | 4000 | 1983 | 1983 | 1983 | 1983 | 
 | W | 3600 | 1986 | 1986 | 1986 | 1986 | 
 | D | 1440 | 1989 | 1989 |  |  | 
 | AN | 2820 | 1993 | 1993 |  | 1993 | 
 | AN | 3030 | 1995 | 1995 | 1995 | 1995 | 
 | AN | 2750 | 1996 | 1996 |  | 1996 | 
 | W | 3460 | 1998 | 1998 |  | 1998 | 
 | AN | 2500 | 2000 |  |  |  | 
 | AN | 3075 | 2006 | 2006 | 2006 | 2006 | 
 |  |  | 13 | 11 | 6 | 11 | # years
Tunnel Closure Years Under Recent Proposals